## Slide 1: Data Parallel Computing on Graphics Hardware
Ian Buck
Stanford University
Notes: center this

## Slide 2: Why graphics hardware
Raw Performance:
Pentium 4 SSE Theoretical*
3GHz * 4 wide * .5 inst / cycle = 6 GFLOPS
GeForce FX 5900 (NV35) Fragment Shader Obtained:
MULR R0, R0, R0: 20 GFLOPS
Equivalent to a 10 GHz P4
And getting faster: 3x improvement over NV30 (6 months)
2002 R&D Costs:
    Intel: $4 Billion
    NVIDIA: $150 Million
*from Intel P4 Optimization Manual
GeForce FX

## Slide 3: GPU: Data Parallel
  Each fragment shaded independently
    No dependencies between fragments
      Temporary registers are zeroed
      No static variables
      No Read-Modify-Write textures
    Multiple “pixel pipes”
  Data Parallelism
    Better ALU usage
    Hide Memory Latency
[Torborg and Kajiya 96, Anderson et al. 97, Igehy et al. 98]

## Slide 4: Arithmetic Intensity
Lots of ops per word transferred
Graphics pipeline
  Vertex
    BW: 1 triangle = 32 bytes;
    OP: 100-500 f32-ops / triangle
  Rasterization
    Create 16-32 fragments per triangle
  Fragment
    BW: 1 fragment = 10 bytes
    OP: 300-1000 i8-ops/fragment
Courtesy of Pat Hanrahan

## Slide 5: Arithmetic Intensity
Compute-to-Bandwidth ratio
High Arithmetic Intensity desirable
  App limited by ALU performance, not off-chip bandwidth
  More chip real estate for ALUs, not caches
Courtesy of Bill Dally
Notes: Show Graph of off chip bandwidth graph ( Give data driven argument)

## Slide 6: Brook General purpose Streaming language
Stream Programming Model
  Enforce Data Parallel computing
  Encourage Arthithmetic Intensity
  Provide fundamental ops for stream computing

## Slide 7: Brook General purpose Streaming language
Demonstrate GPU streaming coprocessor
  Virtualize the GPU
    Hide texture/pbuffer data management
    Hide graphics based constructs in CG/HLSL
    Hide rendering passes
  Highlight GPU areas for improvement
    Features required general purpose stream computing

## Slide 8: Streams & Kernels
Streams (Data)
  Collection of records requiring similar computation
    Vertex positions, voxels, FEM cell, …
  Provide data parallelism
Kernels (Functions)
  Functions applied to each element in stream
    transforms, PDE, …
  No dependencies between stream elements
    Encourage high Arithmetic Intensity

## Slide 9: Brook
C with Streams
  Simple language additions for streams/kernels
  API for managing streams
Streams
  float s<200,100>;
  streamread (s, ptr);
  streamwrite (s, ptr);

## Slide 10: Brook
Kernel Functions
  Map a function to a set
    pos update in velocity field
kernel void updatepos (float3 pos<>,
float3 vel[100,100,100],
float timestep,
out float newpos<>) {
newpos = pos + vel[pos]*timestep;
}
updatepos (pos, vel, timestep, pos);
Notes: Bad figure

## Slide 11: Fundamental Ops
Associative Reductions
MyReduceFunc (s, result)
  Produce a single value from a stream
  Examples: Compute Max or Sum
8 | 6 | 3 | 7 | 2 | 9 | 0 | 5
40

## Slide 12: Fundamental Ops
Gather: p = a[i]
  Indirect Read
  Permitted inside kernels
Scatter: a[i] = p
  Indirect Write
ScatterOp(s_index, s_data, s_dst, SCATTEROP_ASSIGN)
  Last write wins rule

## Slide 13: GatherOp & ScatterOp
Indirect read/write with atomic operation
GatherOp: p = a[i]++
  GatherOp(s_index, s_data, s_src, GATHEROP_INC)
ScatterOp: a[i] += p
ScatterOp(s_index, s_data, s_dst, SCATTEROP_ADD)
Important for building and updating data structures for data parallel computing
Notes: Talk about implementation Motivation (not what we can run fast now, but what as fundamental) Ask for trust about with gatherop and scatterop

## Slide 14: Implementation
Streams
  Stored in 2D fp textures / pbuffers
  Allocation at compile time
  Managed by runtime
Kernels
  Compiled to fragment programs
  Executed by rendering quad

## Slide 15: Implementation
Compiler: brcc
foo.br
foo.cg
foo.fp
foo.c
Source to Source compiler
  Generate CG/HLSL code
    Convert array lookups to texture fetches
    Perform stream/texture lookups
    Texture address calculation
  Generate C Stub file
    Fragment Program Loader
    Render code
  Targets
    NV fp30, ARB fp, ps2.0

## Slide 16: Implementation
Reduction
  O(lg(n)) Passes
Gather
  Dependent texture read
Scatter
  Vertex shader (slow)
GatherOp / ScatterOp
  Vertex shader with CPU sort (slow)

## Slide 17: Gromacs
Molecular Dynamics Simulator
7
11
9
15
14
4
16
5
13
19
17
10
20
12
18
21
2
1
6
3
8
Force Function (~90% compute time):
Energy Function:
Acceleration Structure:
Eric Lindhal, Erik Darve, Yanan Zhao
Notes: Lead with this ap.

## Slide 18: Ray Tracing
Tim Purcell, Bill Mark, Pat Hanrahan

## Slide 19: Finite Volume Methods
Wi = ∂W/∂Ii
Joseph Teran, Victor Ng-Thow-Hing, Ronald Fedkiw

## Slide 20: Applications
Gromacs, Ray Tracing:
  Reduce, Gather, GatherOp, ScatterOp
FVM, FEM
  Reduce, Gather
Sparse Matrix Multiply, Batcher Bitonic Sort
  Gather

## Slide 21: GPU Gotchas
NVIDIA NV3x: Register usage vs. GFLOPS
Time
Registers Used

## Slide 22: GPU Gotchas
ATI Radeon 9800 Pro
Limited dependent texture lookup
96 instructions
24-bit floating point
Texture Lookup
Math Ops
Texture Lookup
Math Ops
Texture Lookup
Math Ops
Texture Lookup
Math Ops

## Slide 23: GPU Issues
Missing Integer & Bit Ops
Texture Memory Addressing
  Need large flat texture addressing
Readback still slow
Shader compiler performance
  Hand code performance critical code
No native reduction support
Notes: reduction support for tone mapping

## Slide 24: GPU Issues
No native Scatter Support
  Cannot do p[i]=a (indirect write)
  Needs:
    Dependent Texture Write
    Set x,y inside fragment program
No programmable blend
  GatherOp / ScatterOp
Limited Output

## Slide 25: Status
In progress
  NV30 prototype working
Scheduled public release date
  December 15, 2003
  SourceForge
Stanford Streaming Supercomputer
Cluster version

## Slide 26: Summary
GPUs are faster than CPUs
  and getting faster
Why?
  Data Parallelism
  Arithmetic Intensity
What is the right programming model?
  Stream Computing
  Brook for GPUs

## Slide 27: Summary
“All processors aspire to be general-purpose”
  Tim van Hook, Keynote, Graphics Hardware 2001